## Slide 1
Index slide
Slide Index
3-17 Arduino Specifications and Hardware
18-34 Arduino Install, IDE and Software

## Slide 2: Fall 2018 CAM8302E (Week 3) Microcomputer Interfacing Arduino Overview
Week 3 -- 44 slides Michel Hanbury Sept. 21st 2017

## Slide 3
Arduino Specifications and Hardware

## Slide 4: Arduino Microcontroller
A popular inexpensive microcontroller used for embedded systems. It has 16 (10 bit A/D) inputs and synchronous and asynchronous serial ports. The device has 54 programmable digital I/O pins.

## Slide 5: Arduino Mega Specs:
Indicates amount of memory, I/O pins and basic voltage and current specs.
Flash – non volatile program storage. SRAM – variable storage.
10 bit (0-5 volts)
min
min
max
max
Logic High
Logic Low
Logic Levels

## Slide 6: Arduino Hardware
Serial I/O (0,1)
SPI (19-22)

## Slide 7
Connect to these points to power the circuits on your proto board.
Disconnect the USB cable when making changes to your circuits. (Maximum current 100 mA)
Gnd
+5

## Slide 9
Connect power to your circuit from 5V and ground. Max of 100 mA through +5
The 5 volt pin is an output supply. Do not connect 5.0 volts from a power supply to this pin. Do not connect power to any other pin.
16 analog to digital converter channels (0 to 5.0 volts) 0 to 1023 10 bits 4.88 mV resolution.
Arduino I/O Pins

## Slide 10
Serial I/O
I2C
Main Digital I/O
TTL o/p max. 40 mA
More Digital I/O
Serial I/O
PWM
Arduino I/O Pins

## Slide 11: Arduino Specs:
** Read this section carefully.

## Slide 12: Arduino Specs:

## Slide 13: Arduino Specs:

## Slide 14: Avoid Damaging the Arduino
** Read this section carefully.

## Slide 15
** Read this section carefully.

## Slide 19
Arduino IDE Install and Software
(IDE) Integrated Development Environment
The Arduino IDE is a free open-source program.
The latest version is 1.8.7

## Slide 20: Arduino Board Setup:
The Arduino converts the serial data to USB.
The PC converts the USB data to asynchronous serial.
1
2
3
4
5

## Slide 21
Verify
Upload
New
Open
Save
Arduino IDE (Integrated Development Environment)
Use the IDE to write, debug, verify and transfer your program.
The IDE can be downloaded for free:
(Transfer to Arduino)

## Slide 22
Basic Arduino program structure. Setup() runs once
and the loop() functions runs continuously once started.

## Slide 23: Arduino Program (sketch.ino): Definitions, Libraries, Setup, Loop

## Slide 31: Code that is run only once
The code in the setup() function is executed once and is not part of a program loop.

## Slide 32: Software Example:

## Slide 33
Verify
Upload
New
Open
Save
Arduino IDE (Integrated Development Environment)
Use the IDE to write, debug, verify and transfer your program.
(Transfer to Arduino)
IDE -- Integrated Development Environment

## Slide 34: Arduino Program (is called a Sketch): Definitions, Libraries, Setup, Loop

## Slide 38: Arduino LCD Library

## Slide 39
Many add-in libraries can be found on the GitHub web site.
These libraries are installed using the Arduino IDE.
The Arduino can call functions that are part of the library.