## Slide 1
Slide Index
3-10 Basic I/O Hardware for the Arduino
11-25 LCD Display and Keypad
26-30 Basic Input / Output Circuits and Transistors
31-41 1 Wire Data Communications and the DHT22 Sensor
42-60 I2C and the MCP4725 DAC
61-68 Asynchronous Serial Communications and RS-232
69-75 Arduino and Logic Gate Parameters
76-101 Arduino Software

## Slide 2: Fall 2018 CAM8302E (Week 4) Microcomputer Interfacing
Week 4 – 102 slides Michel Hanbury Sept. 18th 2018

## Slide 3
Basic I/O Hardware for the Arduino

## Slide 4
The first few lines of the Arduino program define labels used later in the program.
For example if the label “GrnLed” is used it is actually replaced with the value 22.

## Slide 5
Configure Input and Output pins. To protect the I/O hardware and the Arduino the I/O pins are defaulted as inputs until the software configures them as outputs.

## Slide 6
Calculations on data from photocell. The code converts the integer value from the A/D converter to a voltage and then to a resistance.

## Slide 7
Control output based on input conditions.
PB1 push button is normally HIGH using a pull up resistor. When the push button is pressed the pins short and a connection to ground is made.
PB2 is normally LOW, a resistor is used to pull the signal to a low and a short on the pin ties it to +5.
Pin 13 L on the board.

## Slide 8
The Arduino Serial monitor can be used to output variable data to a computer screen.
The BPS (bits/second) baud rate must match the configuration in software. In this example the rate is 9600 bits per second.
Serial.println moves to the start of the next line, then prints.

## Slide 9
Check the results based on the code.

## Slide 10
Check the results based on the code.

## Slide 11
LCD Display and 5 key Analog Keypad

## Slide 12
LCD – Liquid Crystal Display
- Low Power (mA)
- Easy to use libraries available
- Inexpensive and common.
- Easy to wire (8 pins)
LCD Display 16 x 2
Liquid Crystal Display (LCD)

## Slide 13
I2C serial
LCD Display
20 char x 4 lines
A special circuit attached to the rear of the display converts the display from parallel to I2C serial. Connecting to this display requires only 4 wires.
The display includes a backlight and a contrast adjust.
LCD Display
20 char x 4 lines
Parallel Interface.
This is the type that comes with the lab kit. It is less expensive and the software is less complex than the I2C type

## Slide 14
Touch colour display. Adds input and output to an embedded system. A great way to create a basic HMI. You can add sliders, gauges and graphics. Programming is more complicated. Most displays have drivers and functions that make programing easier.

## Slide 15
Parallel LCD Display 16 char. By 2 lines.
This LCD display uses a 4 bit parallel interface. The RS and E are signals used to control data.
Only the upper 4 bits of the display are used by the Arduino.
The “E” pin is the clock signal.
The “RS” is the register select and selects between data and control.
The LCD function needs to know which Arduino pins will control the LCD.
2 pins for control and 4 pins for data.
The (16,2) tells the function that the display is 16 character wide and 2 characters high.
The resistor is used to control the display contrast. Some displays include a backlight,

## Slide 16
The LCD display is arranged as 2 rows and 16 columns. The numbering starts at 0 for the rows and columns. The first number represents the column the second the row.
The top left character is at 0,0.
For example 6,1 is the bottom row and the 7th position over.

## Slide 17
The Arduino IDE includes a library for an LCD display with an HD44780 controller. LiquidCrystal lcd(8, 9, 4, 5, 6, 7) defines the pins that are required by the display. The display uses 4 data lines, an enable signal and a RS - register select pin that selects between either data or control signals. The display uses a Hitachi HD44780 controller, this is the most common type. You must include the “LiquidCrystal.h” header file in your Arduino sketch to use the LCD functions.
Arduino LCD Setup()

## Slide 18
The LCD display board also has a set of push button switches which are connected to a set of resistors used in a voltage divider. Pressing different switches will cause the voltage on Analog 0 (AD0) to change. The resistors shown are the actual values used on the board.
The numbers in red are values I found when testing my keypad. The range may vary by +/- 3.
Arduino LCD / Shield Keypad
302
102
331
681
302
3k Ω
330 Ω
680 Ω
1k Ω
3k Ω

## Slide 19
When no buttons are pressed the A/D reads 1023.
The number “3” is at LCD position 3,0.
The letter “E” is at LCD position 3,1.

## Slide 20
Read and display the value from analog input 0.
Arduino LCD / Keypad Shield

## Slide 21
Example – Setup for LCD and I/O

## Slide 22
This program reads the analog 0 input voltage to determine if the sensor voltage.
The program uses a range to determine which key is being pressed.
A range is chosen because the resistor have a tolerance of +/- 5%
Using the push-buttons to make decisions

## Slide 23
Read and display the value from analog input 8.
Example – Using the LCD display to show the value of analog Input 8.

## Slide 24
Example – Using the UP/DN buttons to control Outputs

## Slide 25
Example – Using the LCD display to show the value of analog Input 8.

## Slide 26
Basic Arduino Inputs and Outputs
Transistor Switch

## Slide 28
Off
On

## Slide 29
NPN 2N2222 Transistor Switch – “ON”
Saturation – Transistor is turned on: The collector to emitter junction acts like a closed switch.
The base voltage must be greater than the emitter voltage by 0.8 volts.
The transistor has a gain of about 75.
Example: If the base current equals 3.5 mA and the gain = 75 mA the transistor will allow up to 263 mA of current to flow.
Transistors can only handle a certain amount of collector current specified in the data sheets.
The CE junction does not act like a perfect switch and may have a voltage across the CE junction of about 0.2 volts.
0.8 v
4.2 v
Current Gain:
Ic/Ib
Minimum of 75 for 2N2222
3.5 mA
153 mA
6.11 volts
6.3 volts
CE = 0.2 v
closed

## Slide 30
0 mA
NPN 2N2222 Transistor Switch – “Off”
Current Gain:
Ic/Ib
Minimum of 75 for 2N2222
NPN Transistor Switch off:
Cut-off – Transistor is turned off: The collector to emitter junction acts like an open switch.
The BE voltage must be less than 0.8 volts.
5.0 v
6.3 v
open
0 mA
5.0 V
0 volt drop
6.3 v
0 volt drop

## Slide 31
1 Wire Data -- Temperature and Humidity Sensor
DHT22

## Slide 32
The temperature / humidity sensor connects the Arduino using a 1 wire serial interface. The sensor transmits 32 bits of data representing the % humidity and the temperature in degrees Celsius.
DHT22 Digital Temperature and Humidity Sensor (Serial Data Output)

## Slide 33
The DHT22 temperature and humidity sensor sends a digital pattern to the Arduino representing % relative humidity and temperature in degrees Celsius .
The first 16 bits transmitted represent the humidity, the second 16 the temperature and the last 8 bits are a checksum to verify the data.
DHT22 Digital Temperature and Humidity Sensor (Serial Data Output)

## Slide 34
Data from humidity and temperature sensor.
40 bit data
32 bits of data
8 bit checksum.
16 bits for humidity
16 bits temperature

## Slide 35
DHT22 Example: Digital Temperature and Humidity Sensor (Serial Data Output)

## Slide 36
DHT22 Example: Digital Temperature and Humidity Sensor (Serial Data Output)

## Slide 37
Data from humidity and temperature sensor.
40 bits in total
32 bits of data
8 bit checksum.
16 bits for humidity
16 bits temperature
DHT22 Example: Digital Temperature and Humidity Sensor (Serial Data Output)
This capture shows all 40 bits transmitted.

## Slide 38
Note: scope is set to 100 us /div.
If the bit has about 70 us high it represents a high.
If the data is about 30 us high it is a low.
D7
D0
Humidity
High byte
00000010 = 0x02
low
high
1st of 5 DHT22 Example: Humidity High Byte 0x02 70us (70) and 30 us (low)
0000 0010 0x02

## Slide 39
Humidity
Low byte
01011000 = 0x58
From high + low
0x0258 = 600d
Divide the value by 10 = 60%
D0
D7
2nd of 5 DHT22 Example: Humidity Low Byte 0x58
0101 1000 0x58

## Slide 40
Temperature
High byte
00000000 = 0x00
D0
D7
3rd of 5 DHT22 Example: Temperature High Byte 0x00

## Slide 41
Temperature
Low byte.
11100010 = 0xE2
High + low byte
= 0x00E2
= 226 / 10 = 22.6
D0
D7
4th of 5 DHT22 Example: Temperature Low Byte 0xE2
1110 0010 0xE2

## Slide 42
I2C Eye 2 Sea -- Inter IC communications and the MCP4725 12 bit I2C DAC

## Slide 44
Devices that use I2C

## Slide 45
The I2C bus uses Vcc, ground and 2 signal wires.
SDA – serial data
SCL – serial clock.
The bus is used to connect many devices to the I2C signals on the Arduino or other controllers such as a Rasberry PI low cost computer.

## Slide 46
Each I2C device has a specific 7 bit address to select the I2C device.
In the lab three I2C devices will be used.
A MCP4725 12 bit DAC.
An ADXL345 Accelerometer.
A DS3231 real time clock.
There are many I2C devices that can be connected to the Arduino.
Displays, pressure and temperature sensors, etc.

## Slide 47
I2C Protocol MCP4725 Start, Stop, Address and Data and ACK
The clock signal is used to synchronize the data. The data is sampled and captured on the positive level of the clock signal. Each byte of data includes a start condition, a stop condition and an acknowledge bit that verifies the data transmission.
Start – Clock is high when data changes to a low.
Stop – Clock is high when data goes high.
Stop/Start – only time data changes when clock is high. Normally data is stable when clock is high.

## Slide 48
MCP4725 12 bit DAC Waveform
Data is sampled when clock is high.
First bit is MS.
Bit 9 is the acknowledge bit.
0 is ok ( ACK )
1 is not ok. (NACK)

## Slide 49
MCP4725 12 bit DAC Waveform
The start sequence and stop sequence are special in that these are the only places where the SDA (data line) is allowed to change while the SCL (clock line) is high. When data is being transferred, SDA must remain stable and not change whilst SCL is high. The start and stop sequences mark the beginning and end of a transaction with the slave device.
Device Address
Device Data

## Slide 50
MCP4725 12 bit DAC Waveform

## Slide 55
D7
D6
D5
D4
D3
D2
D1
D0
Ack
Data rate = 100,000 bps.
10 us / bit
MCP4725 I2C DAC
In this example 8 bits of data
10000100 are transmitted. MSB is first.
MCP4725 12 bit DAC Waveform
1
0
0
0
0
0
1
0
ack
msb

## Slide 56
MCP4725 I2C DAC
Data = 0x7AD
First 12 bits of the two byte number
= 1965 decimal
1965/4096
= 0.4797
0.4797 * 5.0 volts
= 2.4 volts.
MCP4725 12 bit DAC (Arduino sketch)

## Slide 57
MCP4725 I2C DAC
Data = 0x900
= 2304 decimal
2304/4096
= 0.5625
0.5625 * 5.0 volts
= 2.8 volts.
MCP4725 12 bit DAC (Arduino sketch)
The DAC Data is transmitted as two bytes (4 nibbles). The first byte represent the 1st 8 bits of the data. The next byte (upper 4 bits) represents the lower 4 bits of the data. There are 12 bits in the data. The MCP4725 address is 0x60.
MCP4725 Addr = 0x60
MCP4725 Command 0x40
DAC value upper 8 bits
DAC low 4 bits

## Slide 58
D7
D6
D5
D4
D3
D2
D1
D0
Ack
Data rate = 100,000 bps.
10 us / bit
MCP4725 I2C DAC
Data = 84
MCP4725 12 bit DAC Waveform

## Slide 59
MCP4725 I2C DAC
Data = FFF
FFF/FFF * 5.0 volts
= 5.0
MCP4725 12 bit DAC Waveform

## Slide 60
MCP4725 I2C DAC
Data = 0x84C
0x84C = 2124 dec
2124/4096 * 5.0 volts
= 2.6 volts.
MCP4725 12 bit DAC Waveform

## Slide 61
Asynchronous Serial I/O and RS-232

## Slide 62
American Standard Code for Information Interchange
The ASCII table shows the standard code used to transfer characters.
Examples: “1” = 0x31, “A” = 0x41 “U” = 0x55 or 01010101 in binary

## Slide 63
An RS-232 serial connector has 9 pins. At least 3 pins are required to transmit and receive data
At TTL level the data begins with a low start bit, 8 data bits and a high stop bit.
To transmit at greater distance RS-232 levels are used. Typical values are +/- 12 volts.

## Slide 65
To convert from TTL levels to RS-232 levels it is common to use a level translator called a MAX232. This chip is manufactured by MAXIM.
The chip converts a logic high (5 volts) to (-12 volts)
A logic low (0 volts) is converted to (+12 volts DC)

## Slide 66
A typical USB to RS-232 converter.
Standard asynchronous serial bit rates.
Putty is a common (free) serial terminal program for a PC or MAC computer. It can be used to receive and transmit serial data from the Arduino or myDAQ to a PC or MAC.

## Slide 67
Many devices used in the electrical industry transmit and receive data using Asynchronous serial transmission. This method of communications requires only 3 wires, TXD, RXD and ground. Data can transmit at rates from 9600 bps to
The receiver and transmitter must operate at the same data rate. One of the more common data rates is 9600 bps. Other “standard” bit/second rates are 1200, 2400, 4800, 19200, 38400, 57600, and 115200.
At 9600 bits/second one data bit takes 104 us.
Start and stop bits are used for synchronization.

## Slide 68
D0
start
stop
One Byte of Data ASCII “V” = 0x56
Start bit is always low, stop bit is always high.
1 byte transmits in 1.06 ms.
That is about 1000 bytes per second.
Not fast enough to send a video but more than fast enough to transmit data such as temperature and humidity.
D1
D2
D3
D4
D5
D6
D7
01010110 = 0x56 = “V”
Asynchronous Serial Data
Asynchronous Serial Data Waveform
This is an example of the ASCII code “V” being transmitted.

## Slide 69
Asynchronous Serial Data -- Example
Asynchronous Serial Data Waveform
This is an example of a message being transmitted. 8, horizontal tab, V,o,l

## Slide 70
Arduino and Logic Gate Voltage Parameters

## Slide 73
When connecting two digital devices you must verify that the input and output voltages will meet the specifications of the two devices. You must check the VOH, VOL, VIH, VIL spec.
VOH – the minimum output voltage from the Gate.
VOL – The maximum gate output voltage.
VIH – The minimum input voltage for the gate.
VIL – The maximum input voltage for the gate.
If the voltages do not meet the minimum or maximum values indicated, the device may not read the voltage as a proper logic high or low.

## Slide 74: Arduino DC Electrical Specs:
VIH, VIL, VOH, VOL DC specs. For the Arduino

## Slide 76
VIH, VIL, VOH, VOL DC specs. For the 74HC04

## Slide 77
Arduino Software

## Slide 78
Under the Tools tab verify that the board type and Port are properly configured. What is the problem with the setup?
Device not connected. No port.

## Slide 79
Proper Configuration Board, Processor and Port Match:

## Slide 80
An Arduino Mega is connected to COM8. What is the problem with the setup?
Upload
Transfer the program to the Arduino
Verify
Check the program for syntax errors.
Verify the program before uploading to the Arduino.

## Slide 81
Arduino.ino file must be inside a folder of the same name.
The first save creates the folder.

## Slide 84
~ 500 ohms outdoors sunny (0.24 v)
~ 6,000 ohms room light (1.9 volts )
~ 50,000 ohms in darkness (4.2 volts)
Lower voltage when
brighter.

## Slide 87
2nd approach

## Slide 88
Voltage increases
when darker.
Voltage increases
when brighter.

## Slide 90
What is the error?
Arduino Compile Errors
Serial should be Uppercase.

## Slide 91
What is the error?
What is the error?
Arduino Compile Errors

## Slide 92
What is the error?
Arduino Compile Errors

## Slide 93
What is the error?
What is the error?
What is the error?
Arduino Compile Errors
Declared humidity a second time.
“Lab 3”
Missing // comment .

## Slide 94
Arduino I/O setup
Pin 4
Digital input
Pin 2
Digital Output

## Slide 95
Arduino I/O setup

## Slide 96
Serial Port
Viewer
Sensor Values and input status.
Thermistor temperature in degC versus resistance in ohms

## Slide 99
https://www.arduino.cc/en/Guide/Libraries

## Slide 100
Serial Port
Viewer
Baud must match setting
in your program.
DHT Library
Sensor Pin (22)
22,DHT22
Library Functions

## Slide 102
https://www.arduino.cc/en/Guide/Libraries
DHT.cpp C++ program code
DHT.h header file