## Slide 11
CAM8302E Fall 2018
Class Notes:
DC Stepper and Servo Motor Controls

## Slide 12
Slide Index (Total 62 slides):
3: Dc motor types – brushed, brushless and stepper.
4: Basic servo description.
5-14: Basic stepper motor information
15-16: Bipolar stepper motors
17-18: Unipolar stepper motors
19-20: Unipolar and bipolar stepper windings
21: Stepper applications
22-32: Unipolar drive
33-34: For loop, Arduino software for unipolar motors.
35-45: Bipolar stepper motor drive
46-48: Inductive protective circuits snubbers, and diode protection
49-61: Servo motors and drive circuits

## Slide 14
A stepping motor is a motor which has the capability of:
rotating in either direction
starting or stopping in various positions
moving the rotor in precise angular increments for each step applied
the motor can be stopped so that is not easily rotated (holding torque).
Stepper Motor

## Slide 15
https://www.youtube.com/watch?v=vxxnPJBxG3M
https://www.youtube.com/watch?v=TWMai3oirnM
https://www.youtube.com/watch?v=KbDPgxHpgAA
Microchip Stepper Motors
How To Mechatronics
Stepper with Arduino
http://howtomechatronics.com/projects/diy-vending-machine-arduino-based-mechatronics-project/
Vending Machine
How To Mechatronics

## Slide 16
Stepper Motors
Permanent Magnet Unipolar Stepper Motor
Unipolar – current flow in only one direction
Bipolar – current flow in two directions

## Slide 17
Inside A Stepper Motor
Stator – Parts that do not rotate.
Rotor – Rotating parts.
Pole/Phase – coil of wire.

## Slide 18
3D Printer Parts for Position
Z – movement
Control (Up/Down)
Y – movement
Control (Fwd/Rev)
X – movement
Control (Left/Right)
Stepper motors
are used in 3D printer to control the X, Y and Z axis position.
The motors are connected to a belt drive or a lead screw.
4th stepper used to drive the
filament to the print head.

## Slide 19
CNC Using 3 Stepper Motors
CNC – computer numerical control
Laser Etcher
PCB etching
Controller for 4 stepper motors.
X
Y
Z

## Slide 20
3D Printer Parts

## Slide 21
Stepper YouTube Videos
https://www.youtube.com/watch?v=vxxnPJBxG3M
https://www.youtube.com/watch?v=MHdz3c6KLrg
https://www.youtube.com/watch?v=t-3VnLadIbc
https://www.youtube.com/watch?v=blJxz28HuQI
https://www.youtube.com/watch?v=dmk6zIkj7WM
https://www.youtube.com/watch?v=eyqwLiowZiU
Microchip Video
Part 2 operation
3D Printer
Part 1 operation
Anaheim Automation
Stepper Animation

## Slide 22
Stepper motors are easy to control with digital / microcontroller boards such as the Arduino or the Raspberry PI.
Stepper motors provide very precise angular positioning.
Speed and direction are easily controlled with digital circuits .
Stepper motors have no feedback and may miss steps under high torque conditions.
Stepper motors often use a switch or sensor to determine a known home position.
DC Stepper Motor

## Slide 23
DC Stepper Motor
The Hybrid type is most common for higher torque and higher speed applications.

## Slide 24
Stepper Motors Types
* May have 5, 6 or 8 wires.

## Slide 25
NEMA – national electrical manufacturers association

## Slide 26
This is a bipolar hybrid stepper.
There are only 4 wires and the rotor has teeth.

## Slide 28
Unipolar stepper motors have 5, 6 or 8 leads.
They all use two coils with a centre tap.
Some steppers have the wires connected internally, others are connected externally.

## Slide 30
Stepper Motor

## Slide 31
A stepping motor is a motor which has the capability of rotating in either direction, starting or stopping in various positions, and moving the rotor in precise angular increments for each step applied. The motor can be stopped so that is not easily rotated (holding torque).
Stepper Motor

## Slide 32
Two Coils of fine gauge wire – Unipolar has a centre tap.
Permanent magnet rotor
No Brushes
Good Holding Torque (not turning)
Rotates at precise angular increments. 1.8 deg, 5.0 deg. 7.5 deg.
Stops and starts quickly
Digital Control of direction and speed.
No Feedback circuit is required.
Stepper Motor Characteristics

## Slide 33
Drive Conveyor Belts
Robotics
Mechanical Positioning
Ventilation/Lighting Control
Camera Controls
Pick & Place Machines
Assembly Lines
Industrial Control
CNC and 3D printers
Stepper Motor Applications

## Slide 34
From NI.com
Stepper Motor
NI – National Instruments
(LabVIEW)

## Slide 35
Bipolar Stepper Motor

## Slide 36
Bipolar Stepper Motor

## Slide 37
Unipolar Stepper Motor

## Slide 38
Unipolar Stepper Motor

## Slide 39
Stepper Motor Wiring
Bipolar Stepper Motor
4 Wires
Unipolar Stepper Motor
5 Wires
Unipolar Stepper Motor
6 Wires

## Slide 40
Bipolar/Unipolar stepper motors.
Unipolar stepper motors require a simpler drive circuit, bipolar stepper motors have higher torque capabilities.
Unipolar – current flow in only one direction
Bipolar – current flow in two directions

## Slide 45
Two Coils, 48 teeth, rotor is magnetized with north and south poles.

## Slide 46
Stepper Motor Applications

## Slide 47: Stepper Motors – Unipolar Drive

## Slide 48
Unipolar Full and Half Step Mode
The Unipolar motor can be operated in full step or half step.
In full step mode one side of each of the two centre tapped coils is turned on.
The motor moves 7.5 degrees / step. There are 4 different discrete steps.
In half step mode two coils are energized and then one is energized in sequence. In this mode the step angle is half the angle as in full step mode. The drawback is that the half step mode has less torque. In half step mode there are 8 distinct steps.

## Slide 49
Half Step Sequence:
Animation of half step sequence. Centre tap pins 1 and 2 are connected to a positive voltage and the a and b pins are grounded.
Half Step Animation

## Slide 50
Half and Full Step Sequence Unipolar
Full step – always two coils turned on. Has better torque but less step resolution.
Half step – one or two coils turned on. Has reduced torque but greater step resolution.
8 step sequence
1 step sequence

## Slide 51
Full Step Sequence Timing Diagram:
Stepper Full Step Sequence Unipolar Motor
Full Step Sequence:
With a 7.5 degrees/step motor this sequence will take 48 steps to complete one revolution(360 degrees). The full step sequence must be repeated 12 time for 1 revolution.

## Slide 52
Half step sequence has the highest resolution and is most stable at higher speeds.
Half step twice the resolution as full step. ( degrees / step )
Stepper Motor

## Slide 53
Timing Example 1:
Determine the time required per step to rotate a stepper motor at 80 RPMs in half step sequence.
Unipolar Half Step Mode
Step 1: With a 7.5 degrees/step motor this sequence will take 96 steps to complete one revolution.(360 degrees ÷ 3.75/step = 96).
Step 2: Convert the RPMs to RPS(rotations per second) divide by 60.
80 RPM/60 = 1.333 RPS
Step 3: Determine the number of steps / rev. in half step mode. = 96
Step 4: Convert the RPS to time / rotation ( 1/RPS) 1/1.333 RPS = 0.75 sec/rev
Step 5: Divide the time/rev by the steps/rev 0.75 sec/rev ÷ 96 steps/rev = 7.81 ms
Time / step = 7.81 ms./step Result 96 steps x 7.81 ms/step = 0.75 seconds.

## Slide 54
Full / Half Step Sequence Timing another example:
Unipolar Full/Half Step Sequence
In full step mode coils are on for 2 steps then off for 2 steps, this mode produces more torque.
In half step mode a coil is on for three steps then off for five. This mode has twice the resolution for a given stepper motor.
Full 4 Step and Half 8 Step Pattern:

## Slide 55
The ULN2003A is a driver IC. The input is a low voltage, low current digital signal. The IC is capable of driving output loads of higher currents and voltages.
Unipolar Stepper Motor Driver

## Slide 56
ULN 2003A Driver IC
This IC drives inductive loads such as DC motors, solenoids and relays.
The output of the circuit includes suppression diodes to prevent damage to the electronics. The device that appears as an inverter is actually a Darlington Pair transistor drive circuit. When the input is a logic high the output is driven to 0 volts. The Darlington Pair transistor has a much greater Beta than a single NPN transistor.
The input is typically less than 1 mA. Output can handle at least 100 mA per channel.
Unipolar Stepper Motor Driver

## Slide 57
For Loop – Used in Stepper Program

## Slide 58
Arduino Control of a Unipolar Motor in Full Step

## Slide 59: Stepper Motor – Bipolar Drive

## Slide 60
Bipolar Stepper Motor
The Bipolar stepper motor has only 4 wires.
Since the full coil is energized it has a higher torque then the unipolar motor.
The J835L motor used in the lab was modified to operate as a bipolar so that it can be controlled with a bipolar motor controller module. The white wire was cut on both coils.
The DRV8825 is a bipolar stepper motor driver. The driver requires only a step and direction control signal.

## Slide 61
Bipolar DC Stepper Motor Controller

## Slide 62
Bipolar DC Stepper Motor Controller

## Slide 63
The top signal is measuring one of the outputs from the stepper motor. The bottom trace is the step signal. The signal is from the stepper control.

## Slide 65
Stepper Half Step Sequence Unipolar Stepper

## Slide 66
Stepper CW and CCW Direction
Controller clock signal compared to coil signal.
The output changes on the rising edge of the clock.
There are 4 clock periods for 4 steps. One high and one low on the coil represents four steps.
4 steps * 7.5 deg./step = 30 degrees.

## Slide 67
Stepper CW and CCW Direction
CW direction: (direction = 0)
Lower signal rising edge leads the rising edge of the upper signal by 90 degrees.
CCW direction: (direction = 1)
Top signal rising edge leads the rising edge of the lower signal by 90 degrees.

## Slide 68
Interrupts vs Polling
The section of code above uses input polling to test the state of a mechanical switch. If the switch is a logic high an LED is turned on otherwise it is turned off. This method is not efficient and most of the loop time is consumed in testing the switch. If the loop if long then if may take time before the switch is tested and an event may be missed.

## Slide 69
Interrupts Setup
Lines 21-24 configure the interrupt. The program is telling the Arduino that when a rising edge occurs on pin 2 (interrupt 0) then stop what the program is currently doing, execute the “slow” routine then return to where it was before the interrupt.

## Slide 70
Interrupts vs Polling

## Slide 71
Using Interrupts

## Slide 72
Interrupts Syntax

## Slide 73
Interrupts Modes

## Slide 74
Interrupt Program for Stepper P1

## Slide 75
Interrupt Program for Stepper P2

## Slide 76
The two traces above are measuring the signal on the driver outputs connected to the yellow wire and the orange wire.
The direction of current flow in the coil changes on every two steps.

## Slide 77
The two traces above are measuring the signal on the driver outputs connected to the yellow wire and the blue wire.
The two signals are 90 degrees out of phase. When the motor is turning in one direction the signal is leading by 90 degrees, in the opposite direction the signal is lagging by 90 degrees to the other coil.

## Slide 78
The Hall Effect sensor, and the magnet were added to measure the RPMs of the stepper motor. The magnet has three N/S poles that generate three pulses per revolution.

## Slide 79
The motor takes 480 ms. per revolution, 1/480 ms. = 2.08 revolutions per second or about 120 RPM.

## Slide 80
A unipolar stepper requires a simpler driver circuit because coil current flows in only one direction. The bipolar driver requires a dual H-Bridge. This example uses MOSFET transistor which are much more efficient than bipolar transistors.

## Slide 81
Inductive
Load
Back EMF – Back Electromotive Force.
When inductive loads such as relays, solenoids and motors are switched off the stored energy in the magnetic field around the inductor collapses. The collapsing field produces a current in the opposite direction than when the coil is energized. Without the diode a high voltage spike may damage electronic circuits used to drive the coil. Adding the diode provides a path for the current to flow through the diode and the load, preventing damage to the electronic circuits.
During normal operation the diode is reverse biased.
Flyback, Flywheel,Transient Suppression Diode.

## Slide 83
The snubber circuit reduces the peak voltages when an inductive load is removed. If the control is a switch it reduces the spark across the switch. If the control is an electronic circuit (transistor) the snubber prevents damage to the electronics.

## Slide 84: Servo Motors

## Slide 85
Servo Motor – used in robotics and remote controlled devices.
Position is controlled using PWM signal. The motor has a feedback potentiometer to determine the current position of the output control arm. The servo motor moves CW and CCW with about 180 degrees of movement. The servo has a gear train to give it a greater torque.

## Slide 86
Another type of DC motor is called a servo motor. Servos are often used for position control.
A servo motor is controlled using a pulse width modulated signal.
DC Servo Motors

## Slide 87
A servo motor consists of four main sections:
  DC motor
  Gear set
  Potentiometer for feedback.
  Electronic Circuit

## Slide 88
DC Servo Motors
Servo Motor Block Diagram (2nd image)

## Slide 89
A servo motor connects to a controller using three wires.
One of the wires connects to ground a second wire to 4.5 – 6.3 volts DC.
The 3rd wire is the input signal. The signal originated from a controller producing a PWM output signal.
The PWM signal has a period of 20 ms. The time high ranges from about 1 to 2 ms.
DC Servo Motors

## Slide 90
Servo hardware configuration.
Servo Motor Connections to Arduino: Connect the power for the servo to a 4.5 to 6.5 volt battery or DC power supply. The signal controlling the servo motor shaft position is controlled using an Arduino PWM output.

## Slide 91
Smart Servo Motor – used in robotics and remote controlled devices.
Smart Servos communicate between a controller and many servos through a serial link.

## Slide 93
Servo Motor test program.

## Slide 94
Servo motor fully CCW. There are hard limits to the servo position, do not drive the motor to the maximum or minimum positions.
This screen captures shows a time high of ~0.9 ms.
Program Output

## Slide 95
Servo motor at the middle neutral position. This is normally about 1.5 milliseconds.
This screen captures shows a time high of ~1.5 ms.
Program Output

## Slide 96
Servo motor fully CW. There are hard limits to the servo position, do not drive the motor to the maximum or minimum positions.
This screen captures shows a time high of ~2.1 ms.
Program Output

## Slide 97
Screen capture showing the period of the PWM for the Servo. The period equals 20 milliseconds. It is the time high that is changed to control position.

## Slide 98
Pololu DC Motor Controller
DC Motor Controller can handle 12 Amps at 24 volts. Direction and speed control.
Easy interface to PLC, myDAQ or Arduino.